RIGID 55 LOCK ACOUSTIC is a synthetic, decorative, rigid, antistatic floorcovering, available in tiles and planks, with bevelled edges. It consists in a 0.55 mm thick transparent wear layer, a design film, a rigid core board technology and an acoustic underlay integrated reaching 18dB insolation. The overall thickness is 6mm. It benefits from a cross-linked polyurethane surface treatment (PUR+ MATT), making maintenance easier and eliminating the need for initial polishes.

RIGID 55 LOCK ACOUSTIC is an interlocking floorcovering assembled with an interlocking system, resistant to use (commercial / industrial use) of 33 / 42 according to EN-ISO 10874 and has Bfl-s1 class for smoke emission according to EN 13501-1.

RIGID 55 LOCK ACOUSTIC is phthalate free, except recycled content. It is 100% recyclable. It is 100% compliant with REACH. The product emission rate of organic compounds is < 100μg/m3 (TVOC <28 days – ISO 16000-6).